## Port Mapping and Interfacing Specification
### 1. Hardware Configuration
The system utilizes an Intel 8086 Microprocessor interfaced with an Intel 8255 Programmable Peripheral Interface (PPI). The 8255 is configured in Mode 0 (Basic Input/Output) to facilitate communication between the processor and the game peripherals.
### 2. Address Decoding Logic
The 8255 is mapped into the I/O space of the 8086. Address lines A1 and A2 from the microprocessor are connected to the A0 and A1 pins of the 8255, respectively. This alignment ensures that the ports are accessible at even-address offsets, consistent with the 8086 16-bit architecture requirements.
8255 Register	Internal Offset	I/O Address (Hex)	Function
Port A	00	00H	Output to 6 LEDs
Port B	01	02H	Input from 6 Push Buttons
Port C	10	04H	Unused / Reserved
Control Register	11	06H	Initialization / Mode Select

### 3. Port Functional Assignment
#### Port A (Data Output)
- Pins: PA0 to PA5.
- Connection: Connected to 6 LEDs via $220\Omega$ current-limiting resistors.
- Logic: Writing a logic '1' to a bit position illuminates the corresponding LED.
#### Port B (Data Input)
- Pins: PB0 to PB5.
- Connection: Connected to 6 Push Buttons with $10k\Omega$ pull-down resistors.
- Logic: Reading the port returns a logic '1' for a pressed button and '0' for an idle state.

### 4. Control Word Initialization
To satisfy the requirements for Stage 1, the 8255 must be initialized by writing a specific Control Word to the Control Register at address 06H.
- Control Word: $82H$ ($10000010_2$)
- Bit Breakdown:
  - Bit 7 ($1$): Flag set for Mode Set Flag.
  - Bits 6-5 ($00$): Port A set to Mode 0.
  - Bit 4 ($0$): Port A defined as Output.
  - Bit 3 ($0$): Port C (Upper) defined as Output.
  - Bit 2 ($0$): Port B set to Mode 0.
  - Bit 1 ($1$): Port B defined as Input.
  - Bit 0 ($0$): Port C (Lower) defined as Output.

### 5. Signal Interfacing Summary
The interface is completed using the following control signals:
- $\overline{RD}$ and $\overline{WR}$: Synchronize data transfer during I/O instructions.
- M/$\overline{IO}$: Inverted to drive the $\overline{CS}$ (Chip Select) pin of the 8255, ensuring the peripheral is only active during I/O bus cycles.